## Slide 1
Design and Build 2025
Design and Build 2025
MazeBot
Group NO. 17
  Yifan Chen
  Zixuan Wang
  Congbo Li
  Mengdi Yang
  Memebers Cheng Wei
  Yunlu Zhang
    Yanda Shao
    Lirui Pan
    Siyan Wu
  Fuyang Li
    Kuangyu Chen

## Slide 2: Brief Introduction
MazeBot is an intelligent maze exploration robot system based on STM32, integrating fully independently designed technologies such as lidar SLAM, automatic route finding & mapping, precise motion control, and real-time visualization.

## Slide 3: Our Innovation
The mapping algorithm of the upper computer was all handwritten by myself and did not call any Python libraries
A perfect UI interface and a parameter adjustment system tailored to different scenarios
An accurate mileage calculation method was obtained by combining the robot's own mechanical parameters, motor parameters and kinematic formulas

## Slide 4
Content
Software Technical Details
4
5
6
System integration and optimization
Epilogue
Autonomous Robot Hardware Architecture
1
2
3
Firmware Technical Details
Upper-Lower Computer Collaboration Architecture

## Slide 5
Part
01
Autonomous Robot Hardware Architecture

## Slide 6: Design Process

## Slide 7: Hardware Architecture
1.1 Main Controller
STM32 Microcontroller - Core Processing Unit
FreeRTOS RTOS - Real-time Multi-tasking
Task Priority Management:
Priority 4 (Highest): Bluetooth Control, Motor Control
Priority 3 (High): IMU Data Acquisition, LiDAR Processing
Priority 1-2 (Medium/Low): Auxiliary Tasks
1.2 Sensor System
RPLidar C1 Laser Radar
Scan Rate: 10Hz
Range: 0.1-3.5m
Resolution: 360°/rotation
Protocol: Custom Binary
IM948 9-Axis IMU
Update Rate: 250Hz
Data Output: Euler Angles, Spatial Displacement, Quaternions
Feature: Magnetometer Fusion
Encoder System
Independent Wheel Encoders
390 Pulses/Revolution (13 lines × 30 ratio)
Interrupt-driven Counting
1.3 Communication System
HC-04 Bluetooth: 921600 Baud Rate
Multi-UART Architecture:
Bluetooth: Host Communication
IMU: Sensor Data
LiDAR: Scan Data

## Slide 8
Part
02
Firmware Technical Details

## Slide 9: LiDAR Module (LidarModule.h)
Core Functions
Data Packet Parsing: 5-byte RPLidar protocol parsing
Quality Filtering: Filter low-quality points (quality < 5)
Distance Correction:
Linear scaling factor: 0.79
Non-linear close-range correction: Correct distortion within 0.5m
Data Fusion: LiDAR data and odometry data fusion transmission
Technical Features
// Data packet structure (18 bytes)
struct BluetoothLidarPacket { uint16_t header; // 0xAA55 uint32_t angle_deg_q8; // Angle × 256 uint16_t distance_mm; // Distance (mm) uint8_t quality; // Quality (0-63) int16_t odom_x_cm; // Odometry X (cm) int16_t odom_y_cm; // Odometry Y (cm) int32_t odom_theta_deg_q8; // Orientation × 256 uint8_t checksum; // XOR checksum
};

## Slide 10: Motor Control Module (MotorControl.h)
PID Control System
Three-Layer PID Architecture
Heading Loop: Angle Error → Target Speed Difference
Speed Difference Loop: Speed Difference → Duty Cycle Difference Steering Loop: Angle Error → Duty Cycle
PID Parameters
cpp
// Heading Loop
#define KH_P 2.0, KH_I 0.0, KH_D 0.1
// Speed Difference Loop
#define KV_P 3.0, KV_I 0.0, KV_D 0.1
// Steering Loop
#define KT_P 0.4, KT_I 0.0, KT_D 10.0
Motion Control Modes
Control Strategies
Open-Loop Control: Basic direction control
Closed-Loop Control: Precise distance/angle control
Precision Commands
F50: Forward 50cm
L90: Turn left 90°
R45: Turn right 45°

## Slide 11: Encoder Odometry Module (EncoderModule.h)
Differential Wheel Odometry Algorithm
Physical Parameters
cpp
#define WHEEL_DIAMETER 0.065 // Wheel diameter 65mm
#define WHEEL_BASE 0.100 // Wheel base 100mm
#define TICKS_PER_REV 390 // Pulses per revolution
#define ENCODER_SCALE_FACTOR 0.534 // Accuracy correction factor
Calculation Principle
4-Step Processing Pipeline
Read Encoder Increments - Capture pulse counts from both wheels
Convert to Linear Distance - Transform pulses to actual wheel movement
Differential Calculation - Compute robot center movement using differential drive kinematics
World Coordinate Update - Combine with IMU orientation for global position tracking

## Slide 12: IMU Data Processing (im948_CMD.h)
Data Fusion Strategy
Multi-Sensor Integration
Encoder Odometry: High-precision short-distance displacement
IMU Orientation: Accurate angle information
Timestamp Synchronization: 100-data point circular buffer
Independent Odom Transmission
High-Performance Data Stream
11-byte Independent Packet (0xBB55 header)
250Hz High-Frequency Update
Zero-Delay Pose Transmission

## Slide 13
Part
03
Upper-Lower Computer Collaboration Architecture

## Slide 14: Role Split: STM32 vs Python
Lower Computer (STM32)
Real-time Sensor Acquisition:Collects raw data from IMU, LiDAR, and encoders.
Motor PID Control: Executes precise, real-time motion commands.
Encoder Odometry: Calculates robot's position and orientation.
Bluetooth Communication: Handles low-level data transmission and command responses.
Upper Computer (Python)
Live Visualization: Renders sensor data and map in real-time.
SLAM Algorithm: Constructs and updates the environment map.
Path Planning: Makes high-level navigation decisions.
User Interface: Provides controls for parameter tuning and robot command.
A clean division of labor for a tightly coupled system.

## Slide 15: Layered Data Flow Pipeline
From raw sensors to actionable UI, a journey through the system's core.
1. Sensor Layer
IMU, LiDAR, Encoder (Data Origin)
2. Firmware Processing
Multi-tasking & Data Fusion on STM32
3. Communication Layer
Bluetooth Transmission & Data Packet Delivery
4. Software Processing
Real-time Mapping & Algorithm Computation
5. UI Layer
Visualization Control & Parameter Adjustment

## Slide 16: Lightweight Packet Blueprint
LiDAR Fusion Packet
For scan-synced odometry.
Header: 0xAA55
Payload: Angle, Distance, Quality, Odometry
Size: 18 bytes
Frequency: 10 Hz
Standalone Odom Packet
For high-rate localization.
Header: 0xBB55
Payload: Position, Orientation
Size: 11 bytes
Frequency: 250 Hz
Control Command Packet
For motion and system tasks.
Format: ASCII String
Examples: W/S/A/D, F50, L90, x, S
Size: Variable
Type: Human-readable

## Slide 17: Realtime & Sync Tactics
Guaranteeing Real-Time Performance
STM32 Firmware
Utilizes a priority-based RTOS to ensure critical tasks (motor control, odometry) are executed with minimal jitter.
Python Software
Employs a dedicated RX thread to prevent data loss and maintain UI responsiveness during heavy computation.
Communication
UART baud rate is maximized to 921600 to create a high-throughput, low-latency link.
Maintaining Data Synchronization
Timestamp Alignment
MU data is buffered and synchronized with LiDAR scan data to ensure a consistent snapshot of the robot's state.
Pose Interpolation
High-frequency odometry allows for pose correction even as the LiDAR scan is being received, preventing map distortion.
Coordinate Unification
Automatic conversion from the LiDAR's left-hand coordinate system to the screen's right-hand system is performed.

## Slide 18
Part
04
Software Technical Details

## Slide 19: Visualizer Engine Architecture
A multi-threaded design in lidar_visualizer.py for maximum performance.
1. Data Reception Thread
An independent thread solely responsible for reading and parsing data from the serial port to prevent I/O blocking.
2. Main Thread
Handles real-time visualization rendering and SLAM processing, ensuring the GUI remains fluid and responsive.
3. Shared Odom Data
A thread-safe buffer that allows the RX thread to deposit odometry data for the main thread to consume without race conditions.
Performance Metrics
166Hz
UI Update Frequency
15k
Data Packets per Frame
Independent thread processing
Multi-Core Utilization

## Slide 20: SLAM Algorithm (SimpleGridSLAM Class)
Grid map construction
Map size: 500×500 raster
Resolution: 5cm per grid
Probability Update: Cumulative weight of obstacles
Intelligent filtering
Rotation detection filtering: Prevents trailing in mapping during rotation
Motion prediction filtering: Eliminate historical point trailing
Overlap protection mechanism: Protecting the characteristics of the real environment
Coordinate system unification

## Slide 21: Frontier Detection & Selection Logic
Data Preprocessing
LiDAR data undergoes dual distance correction, quality filtering, and time-windowing.
Environmental Perception
Detects open areas (>5m) as potential exits and recognizes obstacles from point clouds.
Path Planning
The A* algorithm plans the optimal route to the selected frontier on the grid map.

## Slide 22: User Interface Feature Set
Real-Time Control Panel
Direction Key Control: Use arrow keys (↑↓←→) for intuitive, real-time motion.
Precision Command Input: Type commands like F50 (forward 50cm) or L90 (left 90°) for exact control.
Parameter Adjustment: On-the-fly tuning of distance scale and short-range correction via sliders.
Map Management
Auto-Save: Maps are automatically saved as .png images and .npy data files.
Metadata Recording: A .json file logs scan statistics and trajectory information.
Multi-Format Support: Ensures compatibility for replay, analysis, and sharing without extra export steps.

## Slide 23
Part
05
System integration and optimization

## Slide 24: System integration and optimization
Real-time performance: <5ms position update delay
Accuracy: ±1cm/ m displacement accuracy
Stability: 250Hz IMU update, 10Hz radar scan Robustness: Multi-level data checksum and error recovery
Performance Indicators

## Slide 25
Part
06
Epilogue

## Slide 27
Thank You